## Slide 1: Image Deblurring using Modified Blind- Deconvolution

## Slide 2: BATCH NO:17B Guide: B. Ravikiran
Y.VENKAIAH NAIDU 314126510118
R.NAVATEJA 314126510081
S.ARAVIND BABU 314126510088
R.SARAT KUMAR 314126510080

## Slide 3: Abstract:
Observed images of a scene are usually degraded by blurring due to atmospheric turbulence and inappropriate camera settings. The images are further degraded by the various noises present in the environment and the system. Therefore it is essential to get a sharp clean image from the noisy blurred image. In digital imaging, blurring is a bandwidth reduction of the image due to imperfect image construction process which gives poor image quality. Some blurring always arises in the recording of a digital image. Along with these blurring effects, noise always corrupts any recorded image. Reconstructing process is divided into two categories, first is nonblind in which the blurring function is given and the degradation process is inverted using one of the restoration algorithms and second blind where blurring operator is not known. Deconvolution using blind method is very complex process where image recovery is performed with little or no prior knowledge of the degrading PSF. The PSF re present the impulse response of a point source . In this paper Blind Deconvolution method has been implemented to deblur a single image. SNR value is calculated for the image.

## Slide 4: Goal of the project
The goal of the project is to deblur the blurred image using the blind deconvolution algorithm using PSF and SNR values of the images.

## Slide 5: Producure:
At first the blurred is taken and it considered as the convoluted form.
We calculate SNR value of the initial blurred image.
We will perform blind deconvolution to the blurred image by estimating different PSF values.
For every PSF values we will generate a image and calculate its SNR value.
We will compare the SNR values of the generated images and the highest SNR value image is consider as output.

## Slide 6: Deconvolution
Deconvolution is to restore or reconstruct the image that has been degraded by convoluting with a known degrading function.
convolution
Deconvolution
f
y
F’
g
g

## Slide 7: Architecture:
Blurred image
Optimized blind deconvolution algorithm
Deblurred image

## Slide 8: Input&output: